## Slide 1
Shyam Bhat
VicharaVandana
CAN –Types of Frames

## Slide 2
Types of CAN Frames
CAN protocol has 4 types of frames.
Data Frame
Remote Frame
Error Frame
Overload Frame

## Slide 3
Data Frame
Frame carrying the data from transmitter node to all receiver nodes.
Serves the main purpose of CAN protocol
Two types of Data Frames
  Standard Frame : 11 bit message ID
  Extended Frame : 29 bit message ID {split as 11 bit Base ID + 18 bit ID Extension}
In CAN when we are normally talking of frames, we are referring Data frames only.

## Slide 4
Remote Frame
Frame Requesting for a Data Frame
A node wants a particular Data frame, so It sends the Remote frame with same Message ID on the Bus.
This remote frame is followed by the Data frame on the bus transmitted by the node who owns that data frame.
Hence Remote frame sending node got the data it requested for.
Now a days Remote frame is obsolete and not used in CAN protocol.

## Slide 5
Error Frame
Error Frame signals an error condition in the data frame being transmitted currently.
If a node detects an error in the data frame being transmitted on the bus currently, then it destroys that data frame and signals all other nodes by transmitting a error frame.
The error can be detected by any of the receiver nodes or the transmitter node.

## Slide 6
Overload Frame
Overload frame is transmitted by a node when it is overloaded and needs some time to process the data frame received previously.
Overload frame format is same as that of an error frame.
Strategy is that since the overloaded node needs some time so it buys that time by keeping the bus busy with its overload frame preventing other nodes to start transmitting data frames.
Maximum of 3 consecutive overload frames can be transmitted by each node after a data frame.