## Slide 1
Flashing process
Realized by: Hayfa Selmi
Reviewed by: Salah Harhira
2023/2024

## Slide 2
I/ Preconditions
II/ PDX charging
III/ FA charging
IV/ TAL generating
V/ ModelStarter
VI/TCF upload and creation
VII/ Start Application, control desk
Summary

## Slide 3
II/ PDX charging:
1) Go to Esys 22.10.00
2) Set the PDX container of the specific SW version and import it into PSDZ
3) “Verbindung schlieben” pop-up appears , click on “Ja”
4) Set the project name
5) Establish the connection
6) Choose the project name that you set in step 4

## Slide 4
I/ Preconditions:
Connect to Hil and check if it‘s in normal status ( contactros closed + 4 DTC in PHEV +5 DTC in BEV)
Stop the TCF file in ECU
Set the PAD diag mode in control desk and open the contactors

## Slide 5
IV/ TAL generating:
Generate TAL from Pdx container
Click on Next
Choose the diagnose adresse “ 07“
Choose the appropiate SWFL option which you can find it located in the software folder C:\_git_tm\DATA\SME_SW\Gen5_PHEV\BMU_PHEV_R39_2251_9_010_C\PstInfos
Add the CAF
If an error message appears, then press ok
Ignore the alert If CAF is added correctly, there is only 1 WARN event.
Select TAL , click on SVT lessen (ECU) and start flashing -> Running

## Slide 6
III/ FA charging:
Import FA file from the software folder C:\_git_tm\DATA\SME_SW

## Slide 10
V/ ModelStarter:
Choose the the model M05 , the specific variant and apply it
1

## Slide 11
Import the new TCF file, if you don‘t find it you can proceed those steps below to create it (methode available only for Gen5 ):
VI/ TCF upload and creation:
b. Run the buildConfig.pkg
c. Choose the specific variant (SE10, SP54…)
Check first the SW exist in the SME-SW folder
d. Select the SW version
e. Select the model M05 (pop-up apears only on the Hil) or choose the first option if you already uploaded the model
f. Go to the configuration folder and you will find the TCF created

## Slide 12
VII/ Start Application, control desk:
Get Started to Wohnen mode and close the contactors

## Slide 13
Thank you !
